## Slide 1
LIGHTWEIGHT PREFETCH-RESILIENT LLC REPLACEMENT POLICY
Presentation by Sharma Chirag
Roll No. : S20240010223
Guide : Dr . Bheemappa Halavar

## Slide 2
Overview
Literature Review
01
Problem Statement
02
Objectives
03
Progress Achieved so far
04

## Slide 3
Literature Review
Paper 1: Drishti — MICRO 2025
  Proposes per-core Global Prediction History Table (GPHT) for reuse prediction
  Introduces Dynamic Sampled Cache Selection — tests multiple policies on sample sets and picks the best
  Key insight: Modern LLCs are sliced; replacement policies must account for per-core behavior
  Not a replacement policy itself — works as a framework with underlying policies (Mockingjay, Hawkeye)
  Gap identified: Drishti does not explicitly distinguish prefetch vs. demand blocks; prefetch-awareness must come from the underlying replacement policy.
Paper 2: PACMan — IEEE Computer Architecture Letters, 2023
  Explicitly addresses prefetch-demand interaction at LLC level
  Proposes tracking prefetch accuracy to modulate insertion/promotion policies
  Demonstrates that prefetch-oblivious policies leave significant performance on the table
  Gap identified: PACMan's accuracy tracking requires additional counters and sampling logic. There is no study of whether a simpler mechanism (e.g., insertion priority alone) can capture most of the benefit at zero overhead

## Slide 4
Gap | Source
No lightweight, zero-overhead prefetch-resilient LLC replacement design exists | PACMan
Drishti's framework does not handle prefetch type needs underlying policy support | Drishti
Prefetch–replacement interaction is understudied in shared multicore LLCs with heterogeneous workloads | Drishti, PACMan
Summary of Gaps

## Slide 5
Problem Statement
  Aggressive hardware prefetching can pollute the Last-Level Cache by filling it with speculatively fetched blocks that are never accessed. In shared multicore LLCs, this pollution is amplified as multiple cores prefetch simultaneously, causing eviction of useful demand data and increasing miss rates.
  Existing solutions either:
  Ignore the problem (standard LRU treats prefetch and demand equally)
  Add significant hardware (PACMan: accuracy counters and sampling logic; Drishti: GPHT tables + sampled cache selection)
  There is a need for a lightweight, zero-overhead mechanism that can reduce prefetch pollution in shared LLCs without requiring additional hardware structures, training periods, or workload-specific tuning.

## Slide 6
Objective
1. Design a Zero-Overhead Prefetch-Aware LLC Replacement Policy
- Modify LRU insertion to differentiate prefetch blocks (low priority) from demand blocks (normal MRU priority)
- Promote prefetched blocks to MRU only on hit (proving they are useful)
- Achieve this using only the existing `access_type` flag — no new hardware tables or counters
2. Evaluate Across Diverse Workload Types and Multicore Configurations
- Test on compute-bound (perlbench), mixed (gcc), and memory-bound (mcf) SPEC CPU traces
- Evaluate in both single-core and 4-core shared LLC configurations
- Measure IPC improvement, LLC MPKI, and a new metric: prefetch usefulness (promoted prefetches / total prefetch fills)
3: Characterize When Prefetch-Aware Insertion Is Effective vs. When It Is Not
- Quantify prefetch usefulness across workload types to understand when the policy helps
- Demonstrate self-adaptive behavior — the policy automatically adjusts based on whether prefetches receive cache hits
- Provide guidance on when lightweight prefetch-awareness suffices vs. when more complex policies (Drishti, PACMan) are needed

## Slide 7
Progress Achieved so far
SETUP & IMPLEMENTATION
- ChampSim environment configured (WSL2) with baseline and prefetch-aware binaries (1-core & 4-core)
- Custom replacement module: lru_prefetch_aware (lru_prefetch_aware.h, lru_prefetch_aware.cc)
- Three key functions: find_victim(), replacement_cache_fill(), update_replacement_state()
Trace Type Baseline IPC Prefetch-Aware IPC Prefetch Usefulness
perlbench Compute-bound 2.158 2.159 (+0.05%) 0%
gcc Mixed 1.967 1.976 (+0.46%) 35.0%
mcf Memory-bound 0.0743 0.0743 (+0.07%) 0.2%
SINGLE-CORE RESULTS:

## Slide 8
Result
1-CORE MCF LONG RUN (10M instructions):
Metric Baseline LRU Prefetch-Aware LRU
IPC 0.0813 0.08127
LLC Misses 834,521 834,918
Prefetch Usefulness N/A 0.19% (1 of 538 useful)
4-CORE HETEROGENEOUS (gcc + mcf + perlbench + gcc), Shared 8MB LLC:
Core Trace Baseline IPC Prefetch-Aware IPC
CPU 0 gcc 1.970 1.971
CPU 1 mcf 0.0847 0.0856
CPU 2 perlbench 2.027 2.17
CPU 3 gcc 1.985 1.996

## Slide 9
4-Core LLC Statistics:
Prefetch fills: 6,475
Promoted (useful): 2,088
Usefulness: 32.2%
mcf load misses reduced by 226 (318,629 → 318,403)
KEY FINDING: SELF-ADAPTIVE WITHOUT ANY PREDICTOR
gcc (stride-friendly) mcf (pointer-chasing)
Prefetch arrives → Insert LOW Prefetch arrives → Insert LOW
Gets HIT (35%) → Promote to MRU No hits (0.2%) → Stays near LRU
Result: IPC +0.46% Result: Demand data protected

## Slide 10
Remaining work
1. Compare with DRRIP, SHiP, SRRIP
2. More aggressive prefetchers (SPP/AMPM at LLC level)
3. Larger instruction windows (50M+ runs)
4. Adaptive insertion position (lightweight dynamic counter)
5. Drishti integration (per-core reuse prediction + prefetch-awareness)
6. Final report and analysis

## Slide 11
Thank You